Certified Copy

____________

Lianne Bedard

Town Clerk

HARTFORD
MAINE

# *ROAD STANDARDS

# THIRD EDITION

# CONSTRUCTION STANDARDS ORDINANCE FOR NEW ROADS

# ARTICLE I.  Purpose

The purpose of this Ordinance is to promote the health, safety and public welfare of the residents of Hartford through establishing minimum construction standards for roads.

# ARTICLE II.  Authority, Administration and Effective Date

# This Ordinance is enacted pursuant to Title 30-A, M.R.S.A. Section 3001, rule.

This Ordinance shall be administered by the Planning Board, in conjunction with the Road and Budget Committee.

The effective date of this Ordinance is March 12, 1988.

ARTICLE III.  Applicability

This Ordinance shall apply to:

A.  All road construction, public or private, intended for public use, defined as any road or way which serves as principal access for five or more different lot owners.

B.  All roads proposed as town ways after the effective date above.

D.  Private driveways serving one to four lot owners are not covered by this Ordinance. A driveway serving as principal access for five or more different lot owners shall be considered intended for public use, except as provided in Part G of this Article.

E.  Alterations and extensions of existing roads by any person or group other than the Town of Hartford shall be consistent only with Article

F.  If the road frontage of a new lot created after March 11, 1989, is located on any right-of-way intended for public use, as this phrase is defined in this Ordinance, such as:                 1. a public easement;                                                                  2. a discontinued road over which a public easement still exists; or                                   3. an abandoned road over which a public easement exits

then such road or way must be altered, improved or extended until it meets standards in Article IV. or V. as follows:

Article IV. applies if the road or way to be altered connects with a paved town road or state road.

Article V. applies if the road or way to be altered connects with a gravel surface road.

# ARTICLE IV.  Minimum Design and Construction Standards

|  |  | Collector | Local |
| --- | --- | --- | --- |
| A. | Minimum width of right-of- way | 66 feet | 50 feet |
| B. | Minimum travel way | 24 feet | 20 feet |
| C. | Minimum width of each shoulder | 7 feet | 5 feet |
| D. | Minimum grade | 0.5% | 0.5% |
| E. | Maximum grade | 9% | 12% |
| F. | Maximum grade at intersections | 2% within 100 ft | 2.5% within 75 ft |
| G. | Minimum angle of intersections | 75 degrees | 75 degrees |
| H. | Minimum center line radii on curves | 200 feet | 200 feet |
| I. | Minimum tangent length between reverse curves | 200 feet | 100 feet |
| J. | Road sub base (maximum stone size of 4 inches) | 18 inches | 16 inches |
| K. | Paving (if specified) | 2.5 in. HTB rolled | 2.5 in. HTB rolled |
| L. | Minimum road crown | .25 inches/foot | .25 inches/foot |
| M | Property line radii | 15 feet | 10 feet |
| N. | Curb line radii at 90 degree intersection Less than 90 degree | 25 feet 30 feet | 25 feet 30 feet |
| O. | Minimum distances between intersections | 200 feet | 200 feet |
| P. | Minimum setback for building construction from center line of road | 58 feet | 50 feet |
| Q. | Minimum building setback at intersection | 80 feet | 70 feet |
| R. | Minimum setback for wood yards | 150 feet | 150 feet |

# ARTICLE V.  General Requirements for All Road Construction

A. Any extension of an existing road shall be at the same or greater width than the existing width.

B. Road names require approval of the Planning Board.

C. All intersections shall be as close as possible to 90 degrees and never less than 75 degrees.

D. Dead end roads shall be marked with a permanent sign and shall be provided at the closed end with a turn-around with a property line radius of at least 70 feet and a traveled way radius of at least 50 feet.

E. Adequate drainage provision shall be made for disposal of all surface water and underground water through ditches, culverts (of standard design and not to include plastic), and/or storm water drainage systems; and catch basins, where necessary. Drainage design shall be based on the 50 year storm event where a stream or brook is involved. All other culverts shall be at least 15 inches.

F. All roads shall be rough graded to the full width of the travel way and the shoulders. Base shall be at least 18 inches.

G. Slopes and ditches shall slope away from the shoulders of the road at a ratio of at least 4 horizontal feet to 1 foot vertical; and never steeper than 2 to 1. In cases where this is not possible or practical, as where the roadway cuts through the side of a hill, all cuts shall be made so that adjacent slopes will not slide. The tops and sides of all cuts shall be cleared of all stumps, trees and boulders for an adequate distance so as to prevent such material from sliding into the ditches. Banks will be loamed; where necessary, seeded and mulched.

H. Paving, when required, shall comply with the following:

1. Paving shall consist of at least 21/2 inches hot top bituminous rolled.

2. Placement of pavement shall conform to Section 403.1 of the State of Maine Highway Commission, Standard Specifications, Highways and Bridges, revisions of June 1968.

I. Graveled surface roads shall conform to the following in addition to all other road standards:

1. Dust from the road will not adversely affect adjacent properties;

2. Surface material shall support anticipated traffic without detrimental deformation;

3. Surface material shall be capable of withstanding the abrasive action of traffic;

4. Surface material shall shed rain; and

5. Surface material shall have capillary action to replace moisture lost by evaporation.

J. Intersections shall have clear sight distance as determined by the Planning Board. Distance shall be in the range of 250 feet minimum to 600 feet maximum. Criteria shall include posted speed limit, type of intersection (whether cross-roads or T) and grade of approaching roads.

ARTICLE VI. Classification of Roads

Roads shall be classified according to the projected volume of traffic, using the number of dwelling units served and other appropriate criteria.

A. Local roads serve 74 dwelling units or less. They may be paved or graveled.

B. Collector roads serve between 75 and 300 dwelling units, or any recreational area with a peak anticipated traffic level of 750 per day or higher. Collector roads must be paved.

C. If a road serves more than 300 dwelling units, or otherwise exceeds 3,000 average daily traffic, then the Planning Board, upon recommendation from an engineer, shall determine the required design standards.

D. Roads intended to serve retail, office, or industrial uses shall be designed by a professional engineer based on detailed traffic analysis.

ARTICLE VII.  Acceptance of Roads by Town

The approval by the Planning Board of a proposed road shall not be considered acceptance of the road by the Town. Final acceptance shall be by affirmative vote at a Town Meeting, provided that 30 days notice of any such Town Meeting shall be given to the Planning Board, Selectmen, Road Commissioner and Budget Committee.

ARTICLE VIII.  Application Procedures

A. Prior to the construction of any new street or the reconstruction or lengthening of an existing street, an application shall be submitted to the Board with the following information:

1. The name(s) of the applicant(s);

2. The name(s) of the owner(s) of record of the land upon which the proposed road is to be located;

3. A statement of any legal encumbrances on the land upon which the proposed road is to be located;

4. The anticipated starting and completion dates of each major phase of road construction; and

5. A statement indicating the nature of traffic expected to be generated by the proposed development expressed in average daily traffic (ADT).

B. The plans and illustrations submitted as part of the application shall be prepared by a Registered Professional Engineer to include the following information:

1. All roadway plan and profile drawings shall be drawn on a scale of 1 inch equals 20 feet - 50 feet horizontal and 1 inch equals 5 inches - 10 inches vertical.

2. The direction of magnetic north.

3. A plan profile and typical cross section views of all proposed roads.

4. The starting and ending point with relation to established roads or ways and any planned or anticipated future extensions of the roads. All terminal points and the centerline alignment shall be identified by survey stationing.

5. The roadway and roadway limit with relation to existing buildings and established landmarks.

6. Dimensions, both lineal and angular, necessary for locating lots, easements and building lines.

7. The lots as laid and numbered on said street, showing the names of owners of abutting property.

8. All natural waterways and watercourses in or on land contiguous to the said road or ways.

9. The kind, size, location, profile and cross section of all existing and proposed drainage ways and structures and their relationship to existing natural waterways.

10. A soil erosion and sedimentation control plan showing interim and final control provisions.

11. Curve data for all horizontal and vertical curves shall be the centerline radius, arc length, beginning of curve and end of curve points.

12. All centerline gradients shall be shown and expressed as a percent.

13. All curve and property line radii of intersections.

14. The limits and location of any proposed sidewalks and curbing.

15. The location of all existing and proposed overhead and underground utilities, to include, but not limited to, the following: (NOTE: When a location, in the case of any underground utility is approximate, it shall be noted on the plan as such.)

A. sanitary sewer lines;

B. storm drains;

C. telephone line poles or underground vaults;

D. electrical power line poles or underground vaults; and

E.	street lights.

16. The name(s) of each proposed new road.

D. An application fee of $200.00 shall be paid to the Town of Hartford upon submission of an application. The Selectmen shall have the authority to review and revise the application fee. Any-fee revisions shall be based on the Town's cost of administration and enforcement or this Ordinance. In addition, the board may require a fee, not to exceed $10,000.00, for an independent engineering review of the site and plans before final approval.

ARTICLE IX.  Application Review

A. Within 30 days from the date of receipt, the board shall notify the applicant in writing either that the application is complete, or, if not complete, the specific additional material needed to make them complete. The Board shall engage an independent Registered Professional Engineer to review the plans and do an onsite inspection, all at the applicant's expense, before final approval. Determination by the Board that the application is complete, in no way commits or binds the Board as to the adequacy of the application to meet the requirements of this Ordinance.

B. Public Hearing: The Board may hold a public hearing within 30 days of having notified the applicant in writing that a complete application has been received, and shall cause notice of the date, time and place of such hearing to be given to the applicant, to all abutting property owners, and published in a newspaper or general circulation in Hartford at least two times; the date of the first publication shall be at least seven days prior to the hearing. Public hearing shall be conducted according to Title 30-A, MRSA, Section 2411, subsection 3a. b. c. d. and e.

C. Application Approval: The Board shall, within 30 days of a public Hearing, or within 60 days of having received the completed application, or within such other time limit as may be mutually agreed, deny or grant approval on such terms and conditions as it may deem advisable to satisfy this Ordinance and to preserve the public health, safety and general welfare. In all instances, the burden of proof shall be on the applicant. In issuing its decision, the Board shall make a written finding of facts, establishing that the applicant does or does not meet the provisions of this Ordinance. The Board must approve the application, if it finds the applicant has complied with all the requirements of the Ordinance.

ARTICLE X.  Performance Guarantee

Prior to final approval of a road design, the board may require that the applicant file with the Selectmen, a performance guarantee sufficient to defray all expenses of the proposed road construction. This may be in the form of one of the following types of guarantees. The conditions and amount of such guarantee shall be determined by the Board with the advice of the various town officials concerned. The amount shall be at least equal to the total cost of all street grading, paving, storm drainage and utilities or other improvements specified on the plan within two years of the date of the performance bond or certified check or irrevocable letter of credit.

Adopted March 12, 1988

All Articles amended March 11, 1989

Amended  Article III. C., and Article VIII. B. 6. & C. June 10, 2010